## Slide 1: binary system
Nirjal Maharjan
BSc.CSIT
022BSCIT024
02/20/2023

## Slide 2: contents
BCD codes 3-5
Error-detection codes 6
Reflected codes 7
Alphanumeric codes 8
  ASCII 9-10
  EBCDIC 11-12

## Slide 3: Binary codes
Binary code are code used in digital computers which are based on a binary number system in which there are only two possible states, off and on, usually symbolized by 0 and 1.

## Slide 4: Bcd(binary coded decimal) codes
Binary coded decimal is a system of writing numerals that assigns a four-digit binary code to each decimal digit from 0 to 9.
Binary coded decimal is a way to convert decimal numbers into their binary equivalents. However, binary-coded decimal is not the same as simple binary representation.
In binary coded decimal, each digits in a decimal base 10 is represented as a group of 4 binary digits, or bits. The code most commonly used for the decimal digits is the straight binary assignment listed in Table.
This scheme is called binary‐coded decimal and is commonly referred to as BCD. Other decimal codes are possible and a few of them are presented later in this section.

## Slide 5: Bcd(binary coded decimal) codes (continued…)
Decimal symbol | BCD digits
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
The table gives the 4‐bit code for one decimal digit. A number with k decimal digits will require 4k bits in BCD.
A decimal number in BCD is the same as its equivalent binary number only when the number is between 0 and 9.
A BCD number greater than 10 looks different from its equivalent binary number, even though both contain 1’s and 0’s.
Moreover, the binary combinations 1010 through 1111 are not used and have no meaning in BCD.
EXAMPLE: Consider decimal 185 and its corresponding value in BCD and binary:
[From the table]
Hence, (185)10 = (0001 1000 0101)BCD = (10111001)2
1 | 8 | 5
0001 | 1000 | 0101

## Slide 6: Error detection codes
Binary information can be transmitted from one location to another by electric wires or other communication medium. Any external noise introduced into the physical communication medium may change some of the bits from 0 to 1 or vice versa.
The purpose of an error detection code is to detect such bit-reversal errors. Error-detecting codes are a sequences of numbers generated by specific procedures for detecting such errors in data.
PARITY CHECK:
One of the most common ways of error detection is by means of a PARITY BIT. This way is called parity check.
A parity bit is an extra bit included with a message to make the total number of 1’s transmitted is odd or even
While transmission of BCD code, the sender counts the number of 1s in it and adds the parity bit in following way:
  In case of even parity: If number of 1s is even then parity bit value is 0. if number of 1s is odd then parity bit value is 1.
  In case of odd parity: If number of 1s is odd then parity bit value is 0. if number of 1s is even then parity bit value is 1.
Odd Parity | 
Message | Parity bit
0000 | 1
0001 | 0
0010 | 0
0011 | 1
Even Parity | 
Message | Parity bit
0000 | 0
0001 | 1
0010 | 1
0011 | 0

## Slide 7: Reflected codes
Reflected code is used to convert continuous or analog information to digital form.
Only one bit in the code group changes when going from one number to the next.
Reflected code is also known as reflected binary code(RBC), or Gray code.
The application of Gray code occurs when analog data are represented by continuous change of shaft position.
Gray code is not weighted that means it does not depends on positional value of digit.
For Example:
The representation of the decimal value "1" in binary would normally be "001" and "2" would be "010". In Gray code, these values are represented as "001" and "011". That way, incrementing a value from 1 to 2 requires only one bit to change, instead of two.
Decimal | Binary | Gray (reflected) | Decimal of Gray
0 | 0000 | 0000 | 0
1 | 0001 | 0001 | 1
2 | 0010 | 0011 | 3
3 | 0011 | 0010 | 2
4 | 0100 | 0110 | 6
5 | 0101 | 0111 | 7
6 | 0110 | 0101 | 5
7 | 0111 | 0100 | 4
8 | 1000 | 1100 | 12
9 | 1001 | 1101 | 13
10 | 1010 | 1111 | 15
11 | 1011 | 1110 | 14
12 | 1100 | 1010 | 10
13 | 1101 | 1011 | 11
14 | 1110 | 1001 | 9
15 | 1111 | 1000 | 8

## Slide 8: Alphanumeric codes
Alphanumeric codes are defined as binary codes used to represent alphanumeric data.
The code write alphanumeric data, including letters of the alphabets, mathematical symbols, numbers, and punctuation marks, in a form that is easily understood by a computer.
The most common alphanumeric codes used these days are ASCII code, EBCDIC code, and UNICODE.

## Slide 9: ASCII code
The full form of ASCII code is the American Standard Code for information Interchange. It is a seven-bit code on the English Alphabet.
ASCII was the first major character encoding standard for data processing. Most modern computer systems use Unicode, also known as the Unicode Worldwide Character Standard. It's a character encoding standard that includes ASCII encodings.
In 1967 this code was first published and since then it is being modified and updated. ASCII code has 128 characters some of which are enlisted below:

## Slide 10: Ascii code
DEC | OCT | HEX | BIN | Symbol | Description
0 | 000 | 00 | 00000000 | NUL | Null char
1 | 001 | 01 | 00000001 | SOH | Start of Heading
2 | 002 | 02 | 00000010 | STX | Start of Text
3 | 003 | 03 | 00000011 | ETX | End of Text
4 | 004 | 04 | 00000100 | EOT | End of Transmission
5 | 005 | 05 | 00000101 | ENQ | Enquiry
6 | 006 | 06 | 00000110 | ACK | Acknowledgment
7 | 007 | 07 | 00000111 | BEL | Bell
8 | 010 | 08 | 00001000 | BS | Back Space
9 | 011 | 09 | 00001001 | HT | Horizontal Tab
10 | 012 | 0A | 00001010 | LF | Line Feed
11 | 013 | 0B | 00001011 | VT | Vertical Tab
12 | 014 | 0C | 00001100 | FF | Form Feed
13 | 015 | 0D | 00001101 | CR | Carriage Return
14 | 016 | 0E | 00001110 | SO | Shift Out / X-On
15 | 017 | 0F | 00001111 | SI | Shift In / X-O

## Slide 11: EBCDIC Code
EBCDIC stands for Extended Binary Coded Decimal Interchange Code.
IBM invented this code to extend the Binary Coded Decimal which existed at that time.
All the IBM computers and peripherals use this code.
It is an 8-bit code and therefore can accommodate 256 characters. Below are given some characters of EBCDIC code.

## Slide 12: EBCDIC code
Char | EBCDIC | HEX | Char | EBCDIC | HEX | Char | EBCDIC | HEX
A | 1100 0001 | C1 | P | 1101 0111 | D7 | 4 | 1111 0100 | F4
B | 1100 0010 | C2 | Q | 1101 1000 | D8 | 5 | 1111 0101 | F5
C | 1100 0011 | C3 | R | 1101 1001 | D9 | 6 | 1111 0110 | F6
D | 1100 0100 | C4 | S | 1110 0010 | E2 | 7 | 1111 0111 | F7
E | 1100 0101 | C5 | T | 1110 0011 | E3 | 8 | 1111 1000 | F8
F | 1100 0110 | C6 | U | 1110 0100 | E4 | 9 | 1111 1001 | F9
G | 1100 0111 | C7 | V | 1110 0101 | E5 | blank | … | …
H | 1100 1000 | C8 | W | 1110 0110 | E6 | . | … | …
I | 1100 1001 | C9 | X | 1110 0111 | E7 | ( | … | …
J | 1101 0001 | D1 | Y | 1110 1000 | E8 | + | … | …
K | 1101 0010 | D2 | Z | 1110 1001 | E9 | $ | … | …
L | 1101 0011 | D3 | 0 | 1111 0000 | F0 | * | … | …
M | 1101 0100 | D4 | 1 | 1111 0001 | F1 | ) | … | …
N | 1101 0101 | D5 | 2 | 1111 0010 | F2 | – | … | …
O | 1101 0110 | D6 | 3 | 1111 0011 | F3 | / |  | 

## Slide 13
Thank you
Nirjal Maharjan
022BSCIT024@sxc.edu.np